## Slide 1: CPU PIPELINE DATAPATH
By: Sungho oh & kevin roxas
ECE 524

## Slide 2: What is cpu pipeline datapath
Allows multiple instructions to be executed at once
Performs 5 stages which are
  Fetch, Decode, Execute, Memory, Write-back
But since we are college students and about to be in debt
  Cheap
    Performing only 3 stage
    Why? More complex more expensive build

## Slide 3: What are the 3 stages?
Get the Data from the Memory(Decode)
Execute the instruction(Execute)
Save the Data into the “Memory”(Memory)

## Slide 4: Get the data from memory
First stage of the CPU DATAPATH is the Decode stage
  Acts as Brain on the CPU
  Access into the RAM/Memory to fetch the source ‘operands’
BRAM
  The user setting constants or the logical values are being held inside the RAM
    Which all it has to do in order to receive data is by sending an address to access the instruction in the memory
  When BRAM is ‘0’ it will read the data from the memory
  Acts like a data storage space that holds information data, or instructions to be used.

## Slide 5: Execute
Arithmetic-Logical Unit
  CPU’s calculator
    Gives two operands and one logical operation for it to compute
  Receives information on the BRAM and performs certain logical operation
  Logical Operations
    Addition, Subtraction, AND, OR, AND NOT, OR NOT, NOR
32 Bits of data and we split it into 3 parts
  15 bits for input A
  14 bits for input B
  3 bits for Control(Opcode)

## Slide 6: Save to data
Where do we save the data to?
  Back to the BRAM
    RAM can be both read and write
      Acts as write back into the BRAM but it overwrites the current constant we are on

## Slide 7: DeMO equipments
Zybo Z7-20
PMOD Seven Segment Display (SSD)

## Slide 8: PMOD Seven segment display
Can display only one digit, but in order to display two
  Must set the “light up” by 20 milliseconds alternating between the two digit lights
Depending on which signal we send, it corresponds on the Seven Segment Display as displayed on the diagram on the right
The signals it receives comes from the code shown below and turns from Binary(input) to Hex then it sends towards the Seven Segment Display

## Slide 9: How this work?
switch(3) is for reset and start
switch(2) for slow and normal clk speed
switch(1) is to show address or value
switch(0) is to show input or output
there is 3 bit program counter in VHDL code is connected to address
  to Block memory and to the ALU designed
while counter is < "111" SSD will show what is happening board
  which is showing value outside of memory
soon as counter became "111", done flag will raise
SSD start showing data inside memory

## Slide 10: now we will demonstrate

## Slide 11: References
https://www.fpga4student.com/2017/07/16-bit-alu-design-in-vhdl.html
https://vhdlguru.blogspot.com/2011/06/vhdl-code-for-simple-alu.html#:~:text=ALU(Arithmetic%20Logic%20Unit)%20is,basic%20block%20in%20any%20processor.&text=The%20input%20signal%20'Op'%20is,be%20performed%20by%20the%20ALU.
https://courses.cs.washington.edu/courses/cse378/10sp/lectures/lec11.pdf
https://digilent.com/reference/pmod/pmodssd/reference-manual
Our codes:
https://github.com/ohho96/csun_ece524_pipelined_cpu